## Slide 1: DATABASE MANAGEMENT
Memory Hierarchy:
  Primary Storage
  Secondary Storage
  Tirtiary Storage

## Slide 2: DATABASE MANAGEMENT
At the lowest level of hierarchy is the Cache .
Part of the processor chip
Capable of holding data or machine instructions
Data in the cache are copy of the certain location of the main memory

## Slide 3: DATABASE MANAGEMENT
The unit of transfer between the cache and the main memory is typically a small number of bytes
Often a m/c cache is divided into two levels
  On- board cache is found on the same chip
  as the microprocessor
  Additional level-2 cache is found on another chip
  Capacity of cache is of the order of few megabytes
  Moving an instruction or data between the main memory takes around 100 nanoseconds

## Slide 4: DATABASE MANAGEMENT
Main memory are available with 10 gigabytes or more
Main memories are random access
One can obtain any byte in the same time
Typical time to access data from main memory is 10 to 100 nanoseconds
Centre of the action is the computers main memory

## Slide 5: DATABASE MANAGEMENT
Virtual Memory –
When we write programs, variables of the program, file reads occupies a virtual memory address space
Many machines have virtual memory as 4 gigabytes
Since size of virtual memory is bigger than main memory, most of the content of the fully occupied virtual memory is stored on the disk.
Virtual memory moves between disk and main memory in entire blocks known as pages in the main memory.

## Slide 6: DATABASE MANAGEMENT
Disks:
  Secondary storage is almost exclusively based on magnetic disk.
  Disks provide in expensive, non volatile storage with random access to pages
  The time to access page depends on its location on the disk
  The access time has three components
    Seek time
    Rotational delay
    Transfer time

## Slide 7: DATABASE MANAGEMENT
Mechanics of disk:
Two principal moving pieces of a disk drive are
  Disk assembly
  Head assembly
The disk controller

## Slide 8: DATABASE MANAGEMENT
Disk controller is a processor capable of
  Controlling the mechanical actuator that moves the head assembly to position the head at a particular radius
  Selecting a surface from which to read or write , selecting a sector from the track on that surface that is under the head
  Transferring the bits from the desired sector to the computer’s main memory, or transferring the bits written from the main memory to the intended sector.

## Slide 9: DATABASE MANAGEMENT
Latency of the disk-
The time between the moment at which the command to read a block is issued and the time that the contents of the block appear in the main memory
  Seek time- The time to position the head assembly at the proper cylinder
  Rotational latency- the time for the disk to rotate so that the first of the sectors containing the block reaches the head
  Transfer time – during which sectors of the block and any gap between them rotate past the block

## Slide 10: DATABASE MANAGEMENT
Writing blocks- Head is used to write the new data in the proper location
Modifying blocks- Read the block into the main memory, make changes to the block, write the new contents of the block onto the disk, verify that the write was done correctly

## Slide 11: DATABASE MANAGEMENT
Tertiary storage:
Slow but highly capacious
Principal kinds of Tertiary storage
  Optical Disk Juke Boxes
  Tape Silos